# Diary for the ESP8266 / MAX31820 Weather Underground Station
This project is a simple, temperature-only weather station that reports to the Weather Underground: https://www.wunderground.com/

It uses an ESP8266 Thing Dev board as the Arduino, and one Max31820 Temperature Sensor to read the ambient temperature. The project is housed in a 3D printed box that has holes at the bottom for the USB power and the temperature sensor.
## 3D Printing and Assembly Instructions
1. I prefer PLA.
2. Print box.stl and boxLid.stl, both parts upside down (that is, with the top touching the print bed). Print without support, raft, or brim.
3. The lid may be a little tight the first few times you slide it in.
## Design Notes
- The box will be put in a very damp environment (outside, under a balcony).
- The box holds an ESP8266 Thing Dev board and MAX31820 temperature sensor.
- It is powered by wall-powered USB, plugged into a nearby all-weather socket.
- The temperature sensor is outside the box and below the board, to minimize the detection of the heat generated by the ESP8266.
- The ESP8266 board is 27mm wide. Add 2 mm clearance, so the box interior is 29 mm wide. The length from tip of pins to good clearance above the headers = about 29 mm, so make the box square.
- From the tip of the ESP8266 board to the flexible part of the USB cable is 100 mm, so make the box 100 mm tall.
- The ESP8266 spec claims an operating temperature range of -40°~125° C, so we shouldn't have any trouble with low or high ambient temperatures here.
## To Do
Write and test the software.
## Diary
7/15 – Built the hardware. Did a couple false starts because I'd forgotten why I was going to use a MAX31820 rather than a DHT22: the DHT22 is a 5.5V part and the ESP8266 Thing Dev is a 3.3V part. Also had forgotten that the 1-wire bus needs an external pullup resistor, so I need to solder something up rather than just using hookup wires with connectors on the ends.
Also found I seem to be out of MAX31280 parts. Need to order more. Stole one from my well depth sensor project.
I soldered the whole thing together: soldering the wires for power and data to either side of the 4.7K ohm pull-up resistor, soldered and heat-shrink-tubing covered the power, data, and ground hookup wires to the 3 pins of the temperature sensor.
Started on the software: I modified my unfinished Well depth sensing Arduino Sketch, because that sketch reads from a set of MAX31820's and posts the results. Managed to run the sketch to print the 1-wire address of the temperature sensor I've soldered together (so Good News: I didn't break or overheat the sensor when soldering it.
Started putting together all the files for a github repository.
2/25 – Added lobes for nails/screws to fasten the box to the wall. Thought about, and initially discarded, the idea of sloping the top (bottom) so rail doesn't collect on the top of the box. If I redo the box, I'll do that plus I'll invert it so the model is right-side up for use (upside-down for printing).
Tried to print, but found after 45 minutes that it seems Cura decided that the box needed to be filled completely. Examining the bad file, I found doing a "Check Geometry" on the box model showed a fusion problem, and doing a Layers view in Cura also showed the problem of filling the entire box – so if I'd checked Geometry or looked at layers (always check layers view), I would have seen the problem without wasting plastic.
Redesigned the box from scratch, making it an angled thing to keep the rain out, and designing it upright, with the understanding that I print it all upside-down.
2/24/2018 – With the snow and iffy weather, an outdoor thermometer sounds useful again.
Increased the horizontal clearance of the door from 0.5mm total (0.25mm each side) to 0.75 mm total (0.375mm per side).
12/2/2017 – Considering different ways to enclose the ESP8266, to keep it dry enough. Thinking about a 3D printed, tube-like box with a slide-snap bottom. Did a quick sketch and printed a short version of the box as a clearance test. Found a couple things to fix.
Did a second iteration. Started a full-sized print. Still need to add something to fasten it to the side of the house.