# Diary for the ESP8266 / MAX31820 Weather Underground Station
This project is a minimal, temperature-only weather station that reports to the Weather Underground, https://www.wunderground.com/ , via WiFi.

It uses a Sparkfun ESP8266 Thing Dev board as the Arduino, and one Max31820 Temperature Sensor to read the ambient temperature. The project is housed in a 3D printed box that has holes at the bottom for the USB power and the temperature sensor.
## 3D Printing and Assembly Instructions
1. I prefer PLA.
2. Print box.stl and boxLid.stl. Print without support, raft, or brim.
3. The lid may be a little tight the first few times you slide it in. It will loosen with wear.
## How to Register your Weather Station
1. Create a free account on Weather Underground, https://www.wunderground.com/
2. Log in to Weather Underground
3. Select, under My Profile, My Weather Stations
4. On the resulting screen, select the Register with WU tab
5. Follow the instructions to register your station, selecting "other" for Station Hardware.
6. Write down the resulting Station ID and Station Key. You will load these into the ESP8266 EEPROM so that the Arduino code doesn't have any private information in it. See instructions in the Arduino code (.ino) file for how to load the WiFi credentials and Station credentials into the ESP8266 EEPROM.
7. After a few minutes, power up your new weather station. It should upload the temperature every 10 minutes.
## Design Notes
- Weather Underground takes temperature in degrees Fahrenheit. The code converts from degrees Celsius (the MAX31820 native form) to degrees Fahrenheit for upload.
- My box will be put in a very damp environment (outside, under a balcony).
- The box holds an ESP8266 Thing Dev board and MAX31820 temperature sensor.
- It is powered by wall-powered USB, plugged into a nearby all-weather socket. My power supply is sheltered from the rain, so it should work fine. It will be interesting to see how it fares this winter. Update: it worked without problems.
- I created a slight slope to the top and bottom of the box by doing a Sweep operation. The slight slope should help keep water from pooling on the top of the box.
- The holes in the bottom lid of the box will pass the USB wire and the wires for the MAX31820.
- The temperature sensor is outside the box and below the ESP8266, to minimize the effect of the heat generated by the ESP8266.
- The ESP8266 board is 27mm wide. I added 2 mm clearance, so the box interior is 29 mm wide. The length from tip of pins to good clearance above the headers = about 29 mm, so I made the box square.
- From the tip of the ESP8266 board to the flexible part of the USB cable is 100 mm, so I made the box about 100 mm tall.
- The ESP8266 spec claims an operating temperature range of -40°~125° C, so we shouldn't have any trouble with low or high ambient temperatures here.
## Soldering the circuit
1. Solder the headers to the ESP8266.
2. Trim and bend the ends of the 4.7K Ohm resistor so it just fits with one end plugged into ESP8266 3.3V pin and the other into the data pin (labeled "4" on the ESP8266).
3. Cut 3 long (100 mm) pieces of hookup wire: Red for power, Yellow for data, and Black for ground. Solder them to the appropriate pins of the MAX31820. See the data sheet or my project photo for the pinout of the MAX31820. https://cdn.sparkfun.com/datasheets/Sensors/Temp/MAX31820.pdf
4. Cut 3 short pieces of heat shrink tubing. Slide one over each of the wires, to cover the soldered parts. Use a heat gun to shrink the tubing.
5. Solder the yellow data wire to the data (pin 4) side of the resistor.
6. Solder the red power wire to the power (3.3V) side of the resistor.
7. Cut the black wire to length and plug it into the GND pin on the ESP8266.
## Diary
October 23, 2021 – The station stopped working in July. Today I looked into it and found the Weather Underground site Certificate had been updated in July. Incorporated the new Certificate's fingerprint into the code and ran it; it uploaded just fine.
October 29 – the redesigned FreeCAD file prints and works great. I tightened the lid clearance so it won't fall out so easily.
October 27, 2020 – Autodesk changed the License terms for Fusion 360, so I'm switching back to FreeCAD, which is open source. I'm redesigning the weather station box from scratch to hopefully make a simpler design.
December 7 – Printed the Weather Station box. It works fine. Replaced the FreeCAD design file with a Fusion 360 design file; updated the .stl files.
December 6 - Finished the first draft of the 3D printed Weather Station box in Fusion 360. It's ready to print.
December 5 – Corrected the current time (millis()) to be unsigned long to match the return value from millis() and to correct some time rollover problems. It seems the code was correct; all I had to do was correct the declaration of nowMs.
Did some simple addition of an offset to the millis() result to test time rollover behavior of the time between Posts code. It succeeded.
Started working on the fix for the station not working if the WiFi Access Point is not available at ESP8266 powerup. Ran the HTTPSRequest Sketch (see notes below), testing the case of the AP not being up at startup (turning on after 5 minutes) – the ESP8266 library worked fine. Added a State to the state machine that's for Waiting For Access Point. Tried it out: it successfully handled powering up followed by the Access Point powering up a minute later.
Wrote a simple UrlEncoder and a unit test for it. The output is:
Output should be URL Encoded 0x01 through 0xff
%01%02%03%04%05%06%07%08%09%0A%0B%0C%0D%0E%0F%00%01%02%03%04%05%06%07%08%09%0A%0B%0C%0D%0E%0F%00%01%02%03%04%05%06%07%08%09%0A%0B%0C%0D%0E%0F...
So it looks like the upper digit isn't coming out correctly. It was a simple typo of >>8 instead of >>4. Fixed that and it ran fine.
Tested the normal running of the Sketch; the upload failed with "Unauthorized". So something's wrong with the urlencodedcat() use. Added a debug print of the Post content: the station ID and password look like they weren't null terminated: they contain piles of garbage characters. Read the function and found I'd forgotten to null terminate the output. Fixed that and the upload worked.
Started recreating the station 3D printed box in Fusion 360. The basic box and nail loops went together quickly. Took several tries at the slot for the case's bottom; I need to do one more try from scratch.
December 4, 2019 – Ran the weather station in my office. Changed the EEPROM to talk to the local SSID rather than the garage SSID. The sketch successfully connects to the local SSID, then says "Failed to connect to weatherstation.wunderground.com port 443". This happens before it even sends the SSL fingerprint. Perhaps the protocol has changed.
Found the URL of the protocol no longer works (404). Searched in vain for the Weather Underground Personal Weather Station protocol specification on the Weather Underground site.
Tried manually accessing the station update url of https://weatherstation.wunderground.com/weatherstation/updateweatherstation.php, and received a "bad request" response. That's good, that I didn't get a Not Found or other error.
Found a likely protocol description at The Weather Channel: https://feedback.weather.com/customer/en/portal/articles/2924682-pws-upload-protocol?b_id=17298, last updated June 2019. The protocol documented there seems unchanged.
Put the new update site in the code and tried it. Same error. Tried HTTP instead of HTTPS. Tried connecting to google.com via SSL. Same error, which suggests the problem is not the protocol, but is something to do with the network stack on the ESP8266.
Started reading the ESP8266 WiFi documentation, and found the WiFiClientSecure constructor is active, and should (likely) be constructed during setup() rather than at global variable initialization time before setup() is called. Changed doHttpsPost() to construct client each time it's called. No change.
Decided I need to back up and get a simple web client working again. Successfully ran the ESP8266 BasicHTTPSClient.ino example, so that shows the board works, but that code is very different than what this Sketch uses.
Once I corrected the fingerprint, I successfully ran https://github.com/esp8266/Arduino/blob/master/libraries/ESP8266WiFi/examples/HTTPSRequest/HTTPSRequest.ino, which uses the same API as this Sketch does/did. The big difference is that the working code uses client.fingerprint() to set the SSL fingerprint to use, while the non-working code uses the – very suspect – client.verify(fingerprint, host).
Updated the fingerprint setting code, corrected the fingerprint for the upload site – which was not the same as the one for the main wunderground.com site – and the Sketch successfully uploaded the temperature!
Implemented corrections to a few easy issues listed in this project's github repository.
December 1, 2019 – I took the station down sometime in the past year. I believe I did it because the station wasn't uploading to Weather Underground at all.
Read through the code, creating a GitHub Issue for each change that should be made.
Found that the SSL fingerprint for Weather Underground's site certificate is out of date; the corresponding SSL Certificate expired in September.
July 27 – Changed the upload interval from 10 minutes to 5 minutes, so Weather Underground won't mark a running station as down. Moved the weather station from the house balcony (which is typically 4 degrees Fahrenheit higher than the ambient air) to a garage wall that's in the shade. Found I forgot to reprogram the EEPROM to have it connect to the garage wifi hotspot. I also bent the sensor so it's a little further from the wall. We'll see if these changes improve the accuracy of the readings.
July 16, 2018 – Used two nails to hang the station on the outside wall of our balcony, reasonably sheltered from the sun. It's uploading just fine, and reads about 2 degrees F higher than a free-standing thermometer on the balcony.
July 15, 2017 – Built the hardware. Did a couple false starts because I'd forgotten why I was going to use a MAX31820 rather than a DHT22: the DHT22 is a 5.5V part and the ESP8266 Thing Dev is a 3.3V part. Also had forgotten that the 1-wire bus needs an external pullup resistor, so I need to solder something up rather than just using hookup wires with connectors on the ends.
Also found I seem to be out of MAX31280 parts. Need to order more. Stole one from my well depth sensor project.
I soldered the whole thing together: soldering the wires for power and data to either side of the 4.7K ohm pull-up resistor, soldered and heat-shrink-tubing covered the power, data, and ground hookup wires to the 3 pins of the temperature sensor.
Wrote the software: I modified my unfinished Well depth sensing Arduino Sketch, because that sketch reads from a set of MAX31820's and posts the results. Managed to run the sketch to print the 1-wire address of the temperature sensor I've soldered together (so Good News: I didn't break or overheat the sensor when soldering it.
Started putting together all the files for a github repository.
February 2 – Added lobes for nails/screws to fasten the box to the wall. Thought about, and initially discarded, the idea of sloping the top (bottom) so rain doesn't collect on the top of the box. If I redo the box, I'll do that plus I'll invert it so the model is right-side up for use (upside-down for printing).
Tried to print, but found after 45 minutes that it seems Cura decided that the box needed to be filled completely. Examining the bad file, I found doing a "Check Geometry" on the box model showed a fusion problem, and doing a Layers view in Cura also showed the problem of filling the entire box – so if I'd checked Geometry or looked at layers (always check layers view), I would have seen the problem without wasting plastic.
Redesigned the box from scratch, making it an angled thing to keep the rain out, and designing it upright, with the understanding that I print it all upside-down.
December 24 – With the snow and iffy weather, an outdoor thermometer sounds useful again.
Increased the horizontal clearance of the door from 0.5mm total (0.25mm each side) to 0.75 mm total (0.375mm per side).
December 2, 2017 – Considering different ways to enclose the ESP8266, to keep it dry enough. Thinking about a 3D printed, tube-like box with a slide-snap bottom. Did a quick sketch and printed a short version of the box as a clearance test. Found a couple things to fix.
Did a second iteration. Started a full-sized print. Still need to add something to fasten it to the side of the house.